## Slide 1: Team 7 Mothership Design
By: Ben Dolin, Elias Ghazal, Brad Lock,
Sarah Rasche, Sean Wan, Veronica Yapriadi

## Slide 2
Placeholder: Outline

## Slide 3
Placeholder: Schedule

## Slide 4
Placeholder: Design Decisions

## Slide 5: Walk around

## Slide 6: Walk around (cont.)
APC 12x6 Propeller
Custom landing gear with 1.5" Diameter Foam Wheel
Flaperon
Easily-open fuselage contains electronics & propulsion system
Modular wings supported with spars

## Slide 7: Walk around (cont.)
Insert
Combined Picture
With
Glider
H-tail with rudder and elevator controls

## Slide 8: Aerodynamics
Cl max = 2.0
Cl cruise = .85
𝛼 = 8 degrees
Cd cruise = .05

## Slide 9: Dynamics and Controls
CXu = -0.07660
CLu = 0.00649
Cmu = 0.00000
CXa = 0.37110
CLa = 4.42922
Cma = -0.34752
CXq = 0.31505
CLq = 6.95617
Cmq = -12.19206
CYb = -0.18753
Clb = -0.00863
Cnb = 0.08919
CYp = 0.04034
Clp = -0.39494
Cnp = -0.12280
CYr = 0.20856
Clr = 0.18759
Cnr = -0.10034
Cm(8.5 deg) = 0 Cl(8.5 deg) = .8

## Slide 10: Feedback control system
Radio Control System
AR8000 8-Channel DSMX Receiver
Visual attitude feedback
Air Data from glider pitot tube before drop

## Slide 11: Structures - Wing Box Characteristics
Wing Box Properties |  | Maximum Loads | 
Area (m2) | .63 | Maximum Bending Load (N) | 331.01
Skin thickness (mm) | 1.8 | Maximum Torsional Load (N) | 1.95
Width (m) | 0.3 | 𝜙max (°) | 0.11
Height (m) | 0.036 | Maximum Wing Root Bending Moment (Nm) | 66
 |  | Maximum Wing Tip Vertical Deflections (cm) | 38.9
Notes: Wing box for analysis assumed to be rectangular cross section to simplify analysis and estimate loads. PLA yield strength 35.9 MPa
https://www.sd3d.com/wp-content/uploads/2017/06/MaterialTDS-PLA_01.pdf
With a bank angle of 85 degrees the max stress experienced on the wing would be 7MPa, well within limits.

## Slide 12: Structures - V-n Diagram
Vspeeds | (m/s) | (kts)
VA | 15 | 29.2
VC | 18 | 35
VS1 | 10.28 | 20
VD | 22.69 | 44.1

## Slide 13: Landing gear
Configuration: Tail Dragger
Height: 12 cm
Width: 5 cm
Material: aluminium 5052
Bending radius: .5 cm
Tail down angle: 11 degrees

## Slide 14: Propulsion - Electric Motor
Rated horsepower | 0.125 hp
Motor efficiency | 8.04 g/W
Motor Kv | 520
Rated voltage | 22.2
Rated number of cells | 4-6s
Weight | 207 g
Manufacturer | SunnySky USA
Requirements:
Required thrust = 6.62N
Max. propeller rotation rate = 12,500 rpm
Selected: SunnySky X3520 Brushless Motor
Overview:
750 gf-thrust brushless motor
Can support up to 6s LiPo cell battery and ESC between 80 A to 100 A

## Slide 15: Propulsion - Battery
Requirements:
Min. endurance = 20 minutes
Max. endurance = 27 minutes (under ideal conditions)
Number of Cells | 6S
Amp Hours | 10000 mAh
Volts | 22.2
Number of Batteries | 1
Weight | 1.189 kg
Height | 65 mm
Length | 156 mm
Width | 53 mm
Selected: Multistar HighMultistar High Capacity 10000mAh 6S 10C Multi-Rotor Lipo Pack XT90

## Slide 16: Propulsion - ESC
Selected: 80-Amp Pro Switch-Mode BEC
Brushless ESC, EC5 (V2)
Specifications:
Can take a 3-6 cell lithium polymer (LiPo) battery and draws up to 22.2V of voltage
Can drive up to 7 analog or 6 digital standard-size servos
Has programmable braking setup
Amperage | 60 & up
Auto Cutoff | Yes
BEC Continuous Current | 5A
BEC voltage | 5.5V Switch-mode
Input Connector Types | EC5, 10AWG leads
Output Connector | 4mm Gold Bullet, 12AWG leads
Overload Protection | Yes
Time Delay Brake | Yes
Notes: BEC = battery eliminator circuit

## Slide 17: Propulsion - Propeller
Requirement:
Max. rpm = 12,500 rpm
Selected: APC 12x6 Propeller
Diameter | 12 in
Pitch | 6 in
Hub Thickness | 0.48 in
Airfoil section | NACA 4412
Twist distribution | Constant
Chord distribution | Linear

## Slide 18
Placeholder: Wiring Diagram

## Slide 19: Mothership Performance with Glider
5 minutes flight time with glider:
Required Battery Weight: 4.206N
Voltage: 18.93 VDC
Current: 46.6 A

## Slide 20: Mothership Performance without Glider
14 minutes powered flight time with glider:
Required Battery Weight: 7.477 N
Voltage: 18.07 VDC
Current: 31.5 A
OVERALL MISSION:
Max Voltage < 22.2 VDC
Max Current < 70 A
Max Weight ≈ 11.65 N

## Slide 21
Placeholder: Cost Analysis

## Slide 22
Placeholder: Build Plan

## Slide 23
Placeholder: Test Plan

## Slide 24: Remaining problems and solution plans
Resize wing
Determine how to connect sections of wing together
Recalculate battery size
More accurately size servos for flaperons

## Slide 25: Conclusion
Moving forward:
General Layout is Final
Ready to start building after final analysis